## Slide 1: Autonomous Hypertension Management
Jordan Swartz, MD, MA

## Slide 2: Design Principles
Do no harm
Deterministic by default
Diverse safeguards
Explicit scope boundaries
Verification before intensification
Every decision is traceable
Earned autonomy
Clinician authority
Notes: No single point of failure
System only does blood pressure management Confirm that is truly uncontrolled BP
System cannot override a physician decision

## Slide 3: Assumptions
Adult patients only (age 18+)
Primary hypertension
Patients already diagnosed by a clinician
English-speaking patients
Non-pregnant patients
Outpatient setting
Appropriate regulatory authorization
Notes: Secondary hypertension is screened for, but the treatment pathways are for primary htn

## Slide 4: Clinical Problems
Identifying and classifying hypertension
Selecting appropriate antihypertensive therapy
Titrating medications to achieve BP goals
Calculating cardiovascular risk to guide treatment intensity
Detecting and managing hypertensive emergencies vs severe hypertension
Ensuring medication adherence
Managing medication side effects
Monitoring for drug-related adverse effects
Identifying resistant hypertension
Screening for secondary hypertension
Notes: The first five are about getting the right treatment to the patient the next five are about keeping the patient safe and on track. 5-10% of hypertensives and 20-30% of resistant cases have a correctable underlying cause.

## Slide 5: Safety Failure Modes – 5 most likely causes of severe harm
Failure | Defenses | Deterministic | Residual
Missed emergency | 5 layers | 3/5 | LOW
Overtreatment → fall | 6 layers | 3/6 | MODERATE
Wrong drug in pregnancy | 6 layers | 3/6 | LOW
Electrolyte abnormality post-uptitration/new drug | 6 layers | 6/6 | VERY LOW
Missed secondary HTN | 6 layers | 4/6 | MODERATE
Notes: For overtreatment->fall, residual risk is MODERATE because it depends on the patient reporting symptoms and completing orthostatic screening The more deterministic layers a failure mode has, the lower its residual risk.

## Slide 6: Architecture
State Machine
Decision Trees
RAG Reasoning
System Orchestrator
Safety Pipeline
Conversation
Tool calling
Clinical education
Symptom recognition
Adherence assessment
Reproductive safety screening
Emergency response
Conversation scope enforcement
Main agent - LLM
Pre and post processing layers (LLM + rules)
Note generator
LLM-as-judge
Ingestion services: Withings, Surecripts, OpenFDA HealthGorilla, RxNorm, external clinical notes
Session summarizer
Clinician dashboard
Follow-up scheduler
Other
Side effect mapping
Lifestyle coaching
Interpret ambiguity
Data Stores
EHR
Operational
Vector
Reference tables
Notes: Single main agent architecture. The patient talks to one agent, sees one personality, has one conversation thread. The guardrail layers are invisible infrastructure
Multiagent disadvantages: Handoff bugs lose context, harder to audit cross-agent decisions
Patient mentions “a little chest tightness” casually to the triage agent. The triage agent notes it but doesn’t escalate (subthreshold). Handoff summary to medication agent says “elevated BP, no emergency.” Medication agent never sees the chest tightness.
In this architecture, can't happen because there’s one context window. Everything the patient says is visible to the one agent that’s reasoning about their care. There’s no handoff to drop.
SYSTEM ORCHESTRATOR (runs parallel to agent, triggered by tool calls) State machine transitions
Decision tree traversal
Invoking RAG reasoning as needed safety pipeline All deterministic. No LLM involved

## Slide 7: Patient Context Injection
## Current Patient Context Name: Jane Smith | Age: 58 | Sex: F Care State: AWAITING_DRUG_EFFECT (since 2026-01-28, 15 days) BP Goal: <130/80 Current Medications: - Lisinopril 20mg daily (ACEi, high dose) — started 2024-03-15 - Amlodipine 5mg daily (DHP-CCB, low dose) — started 2026-01-28 ← NEW Last 3 BP Readings: - 2026-02-10: 142/88 (home) - 2026-02-07: 138/86 (home) - 2026-02-03: 151/94 (home) Adherence: Low risk (screener 0, fills on schedule) CVD 10yr (PREVENT): 14.2% Pending Actions: - Follow-up BP check due: 2026-02-25 (4 weeks post amlodipine start) - Recheck labs (K+, Cr) due: 2026-02-11 ← OVERDUE Active Alerts: - Lab recheck overdue (1 day) Conditions: Essential HTN, Type 2 DM Allergies: None documented
Notes: Situational awareness - this is what the agent sees at the start of every single conversational turn. The LLM is stateless. All "memory" lives in FHIR, the operational DB, and the session/care-thread summaries. Context injection is just querying those stores and formatting the results into the messages array on every turn.
def build_patient_context(patient_id: str) -> str:
patient = fhir.get_patient(patient_id)
state = db.get_patient_state(patient_id) # operational DB
meds = fhir.get_active_medications(patient_id) # enriched with class, tier from reference tables
bp_goal = fhir.get_bp_goal(patient_id)

## Slide 8: Tools
Agent uses tools, the results of the tool use are used by the system orchestrator to handle state machine changes, tree traversal, RAG reasoning, and safety pipeline
State Machine
Decision Trees
RAG Reasoning
System Orchestrator
Safety Pipeline
Notes: How the agent and orchestrator work together.
Agent calls tools — that's what LLMs are good at, deciding when and which tool to call based on conversational context.
Agent doesn't handle what happens after the tool call.
Orchestrator does what code does best — deterministic clinical logic that needs to be auditable and reproducible.

## Slide 9: Tools - Deterministic
record_bp_reading
  validate_bp_reading
  add_bp_observation
  classify_bp(systolic, diastolic)
  db.get_patient_state --- retrieves from state machine
  fhir.get_bp_goal
  fhir.get_recent_bps("pt-123", limit=3)
  is_at_goal(recent_readings, bp_goal, min_readings=3)
  if current_state == "AWAITING_DRUG_EFFECT":
  days_since_change = (now() - state_metadata["therapy_change_date"]).days
    if at_goal and days_since_change >= 14:
  new_state = "AT_GOAL" --- state transition
    elif not at_goal and days_since_change >= 28:
  new_state = "CONFIRMING_UNCONTROL"
{ "state": "AWAITING_DRUG_EFFECT", "entered_at": "2026-02-15T14:30:00Z", "trigger": "therapy_change", "context": { "therapy_change_date": "2026-02-15", "changed_medications": ["lisinopril 10mg -> 20mg"], "decision_tree_run_id": "dt-run-42", "follow_up_due": "2026-03-15", "readings_since_change": 3 } }
Patient State
Notes: What happens inside record_bp_reading — the most common tool call in the system. Patient state is the state machine's memory — it's what makes transitions deterministic rather than relying on the LLM to remember what happened.

## Slide 10
Side Effect Management
assess_symptom
Therapy
evaluate_therapy
execute_prescription
stop_medication
Orders
order_labs
Data Retrieval
get_patient_summary
get_bp_history get_lab_results
get_medication_details
Knowledge
search_guidelines
check_drug_interaction
Escalation
escalate
send_to_clinician
Adherence
administer_adherence_screener
Scheduling
schedule_follow_up
State
update_care_state
Screening
flag_secondary_htn_clue
Tools (additional)
Notes: Through these deterministic tools:
symptoms are evaluated as side effects
prescriptions and labs are ordered
database data are retrieved
guidelines are searched

## Slide 11: Agent cannot
Directly write to FHIR (must go through tools)
Skip safety checks (execute_prescription validates them)
Stop a medication autonomously (always clinician approval)
Override a clinician rejection
Prescribe outside the recommendation pipeline
Change care state directly (only via update_care_state with specific update types)
Access other patients' data
Delete clinical records
Notes: These are architectural constraints enforced by the code.
These aren't prompt instructions
LLM literally doesn't have the function signatures to do these things.

## Slide 12: LLM Roles
Role | Model | Reasoning
Main Agent | GPT-4o | Best tool-calling, fast, empathetic tone, reliable function calling. Patient-facing. Focused prompt
LLM-as-Judge | Claude Sonnet 4.5 | DIFFERENT PROVIDER for model diversity. If GPT-4o has a blind spot, Claude may catch it. Strong structured evaluation. Not speed-critical.
RAG Reasoner | GPT-4o | Same model as agent (shares prompt patterns). Strong citation grounding. Separate system prompt.
Note Generator | GPT-4o-mini | Structured input -> structured output. Template-guided. Runs async. Lower cost for high volume.
Intake Classifier | GPT-4o-mini | Simple classification task. Fastest, cheapest.
Scope Classifier | GPT-4o-mini | Classifies every inbound message as bp_related / emergency / off_topic / ambiguous. Runs before main agent. Fast, cheap, high-volume.
Tone Validator | GPT-4o-mini | Validates response tone against care-state expectations. Low volume (~5-10% of responses).
Notes: **GPT-4o** handles the three roles that need the best reasoning: the conversational agent that talks to patients, the RAG reasoner that generates guideline-cited recommendations. **GPT-4o-mini** handles four high-volume, lower-complexity roles: note generation, intake classification, scope classification on every inbound message, and tone validation as a fallback when rule-based checks are uncertain. These run at about a tenth of the cost.
Shares prompt patterns: how you structure the system prompt, how you ask for JSON output, how you instruct it to cite sources. The patterns validated for GPT-4o for the agent context carry over to the RAG reasoner context.
Intake classifier: Classify this patient message for emergency indicators

## Slide 13: Message Processing Pipeline
PATIENT MESSAGE ARRIVES
↓
PRE-PROCESSING LAYERS (before main agent)
1. Emergency keyword scan (deterministic)
2. Scope & intent classifier
3. Patient context injection
4. Secondary HTN symptom pre-scan (and nudge if necessary)
↓
MAIN AGENT (responses and tool calls)
↓
SYSTEM ORCHESTRATOR (state machine, trees, safety pipeline)
↓
POST-PROCESSING LAYERS (after agent response, before delivery to patient)
5. Tone validator
6. Scope re-check
7. Emergency re-scan
8. PHI / proprietary boundary check
↓
RESPONSE
Notes: This shows the full path a patient message takes through the system. This is the policy architecture — the reason we don't need a 5,000-token system prompt. Each policy is independently testable, they don't interfere with each other, and adding a new policy doesn't bloat the system prompt.
Layer 1 - deterministic keyword scan (e.g. "chest pain”) that fires in zero milliseconds with no LLM dependency
Layer 2 - scope classifier that routes off-topic messages to a redirect template without ever invoking the main agent.
Intent: emergencies
Layer 3 - injects the patient context.
Layer 4 - lightweight regex scan for secondary HTN symptom patterns (sleep apnea, pounding heart) and nudges the agent if it finds something
Layer 5 - checks tone against care-state expectations (crisis response can't be chatty)
Layer 6 - re-checks scope in case the agent drifted. Layer 7 - re-scans for emergency keywords in the response itself
Layer 8 - strips any leaked PHI or internal metadata.

## Slide 14: Context
Layer | Content | Size | Always included?
System prompt | Agent persona, capabilities, instructions, scope rules | ~2,000 tokens | Yes
Patient context | Injected structured context | ~500 tokens | Yes
Current session | All messages in the current session | Variable | Yes
Recent history summary | AI-generated summary of the last 2-3 sessions | ~500 tokens | Yes
Tool results | Results from tool calls in the current turn | Variable | Yes
Care thread summary | AI-generated summary of the full care relationship (updated monthly or after major events) | ~800 tokens | If > 5 sessions exist
Notes: When the context window approaches its limit: older messages in the current session get summarized while keeping the most recent 5 turns verbatim Tool result details get compressed. But the care thread summary is always preserved — it's how the agent remembers that this patient is anxious about polypharmacy, or that they had ankle swelling last month.

## Slide 15: State Machine
Lifestyle only
Awaiting drug effect
Awaiting drug effect
At goal
Confirming uncontrolled
Adherence Intervention
Therapy adjustment
Side effect eval
Possible overtreatment
Resistant hypertension
Crisis
Pending clinician
Confirming uncontrolled
Therapy adjustment
State determines:
Which decision tree to use
Which follow-up schedule to use
How to interpret new BP readings
Notes: State machine is the backbone of the clinical workflow. Every state transition is deterministic and logged. The LLM doesn't decide state transitions — the orchestrator does, based on objective data. Patient's current state determines three things:
which decision tree to use
which follow-up schedule to apply,
how to interpret new BP readings.

## Slide 16: State Machine – Transitions – new patient and stable states
From | To | Trigger
NEW_PATIENT | LIFESTYLE_ONLY | Stage 1 HTN + PREVENT <7.5%
NEW_PATIENT | THERAPY_ADJUSTMENT | Stage 2 HTN or PREVENT ≥7.5%
NEW_PATIENT | AT_GOAL | Already on meds + BP at goal
NEW_PATIENT | CONFIRMING_UNCONTROL | Already on meds + BP above goal
NEW_PATIENT | CRISIS | BP ≥180/120 or emergency symptoms
Stable states |  | 
LIFESTYLE_ONLY | THERAPY_ADJUSTMENT | Still elevated after 3-6 months
LIFESTYLE_ONLY | AT_GOAL | Lifestyle modifications worked
AT_GOAL | CONFIRMING_UNCONTROL | BP rises above goal
AT_GOAL | SIDE_EFFECT_EVAL | Side effect reported
AT_GOAL | POSSIBLE_OVERTREATMENT | SBP <100 or hypotensive symptoms
Notes: Stage 1 HTN with low cardiovascular risk goes to LIFESTYLE_ONLY for 3-6 months
Stage 2 or high risk goes straight to THERAPY_ADJUSTMENT

## Slide 17: State Machine – Transitions – assessment and treatment
From | To | Trigger
Assessment |  | 
CONFIRMING_UNCONTROL | AT_GOAL | White coat effect / transient spike
CONFIRMING_UNCONTROL | ADHERENCE_INTERVENTION | Screener ≥8 or missed pharmacy fills
CONFIRMING_UNCONTROL | THERAPY_ADJUSTMENT | Confirmed uncontrolled + adherent
ADHERENCE_INTERVENTION | AWAITING_DRUG_EFFECT | Adherence improved
ADHERENCE_INTERVENTION | CONFIRMING_UNCONTROL | Improved but BP still above goal
ADHERENCE_INTERVENTION | PENDING_CLINICIAN | Barriers need clinician involvement
Active treatment |  | 
THERAPY_ADJUSTMENT | AWAITING_DRUG_EFFECT | Recommendation executed
THERAPY_ADJUSTMENT | PENDING_CLINICIAN | Needs human judgment (Layer 3)
THERAPY_ADJUSTMENT | RESISTANT_HTN | All 4 resistant HTN criteria confirmed
AWAITING_DRUG_EFFECT | AT_GOAL | BP at goal (≥2 weeks post-change)
AWAITING_DRUG_EFFECT | CONFIRMING_UNCONTROL | Still above goal after drug effect period
AWAITING_DRUG_EFFECT | SIDE_EFFECT_EVAL | Side effect reported
AWAITING_DRUG_EFFECT | POSSIBLE_OVERTREATMENT | SBP <100 or hypotensive symptoms
Notes: The assessment flow is where most of the clinical nuance lives.
From CONFIRMING_UNCONTROL, three paths

## Slide 18: State Machine – Transitions – safety and escalation
From | To | Trigger
Safety monitoring |  | 
SIDE_EFFECT_EVAL | AWAITING_DRUG_EFFECT | Drug changed / switched
SIDE_EFFECT_EVAL | AT_GOAL | Minor side effect, tolerable
SIDE_EFFECT_EVAL | PENDING_CLINICIAN | Serious side effect
POSSIBLE_OVERTREATMENT | PENDING_CLINICIAN | Confirmed overtreatment, downtitrate
POSSIBLE_OVERTREATMENT | AT_GOAL | Transient, readings normalized
Exception / escalation |  | 
RESISTANT_HTN | PENDING_CLINICIAN | Specialist referral
PENDING_CLINICIAN | AWAITING_DRUG_EFFECT | Clinician approved therapy change
PENDING_CLINICIAN | AT_GOAL | Clinician determined no change needed
Notes: Safety monitoring states handle the things that can go wrong during treatment.
The exception states: RESISTANT_HTN always goes to PENDING_CLINICIAN for specialist referral. PENDING_CLINICIAN resolves when the clinician either approves a therapy change — AWAITING_DRUG_EFFECT — or determines no change is needed — AT_GOAL

## Slide 19: State Machine – Transitions – crisis
From | To | Trigger
Crisis (universal — from any state) |  | 
LIFESTYLE_ONLY | CRISIS | BP ≥180/120 or emergency symptoms
AT_GOAL | CRISIS | BP ≥180/120 or emergency symptoms
CONFIRMING_UNCONTROL | CRISIS | BP ≥180/120 or emergency symptoms
AWAITING_DRUG_EFFECT | CRISIS | BP ≥180/120 or emergency symptoms
SIDE_EFFECT_EVAL | CRISIS | Dangerous reaction
POSSIBLE_OVERTREATMENT | CRISIS | Syncope or fall
CRISIS | PENDING_CLINICIAN | Always (immediate clinician notification)
CRISIS | AWAITING_DRUG_EFFECT | After crisis resolved + therapy adjusted
Notes: Crisis is a universal override — any state can transition to CRISIS when BP is at or above 180/120 or emergency symptoms are detected
This is enforced deterministically: the BP classification runs on every recorded reading, and the emergency keyword scan runs on every inbound message.

## Slide 20
Notes: The state machine captures the reality that hypertension management is non-linear
Green for stable/goal states
blue for entry and active treatment
yellow for assessment and confirming
orange for safety monitoring
red for exception and escalation states.

## Slide 21
Decision Tree Selection
1. Care state selects the entry point
Initial therapy, uncontrolled monotherapy, or uncontrolled combination therapy.
2. Verify the clinical context
Use structured observations, medication history, adherence, and relevant laboratory data.
3. Resolve each decision node
Record the question, answer, source data, and confidence for the audit trail.
4. Escalate unresolved decisions
Missing data or clinical judgment routes to retrieval with citations or clinician review.
Notes: This slide summarizes the proposed decision-tree mechanics from architecture.md, Sections 2 and 13. Care state selects the entry tree. Each node records its evidence and answer. Unresolved decisions route to retrieval with citations or clinician review. This is a design specification, not a validated clinical protocol.

## Slide 22
From Tree Output to a Proposed Prescription
1. Select a drug class
The tree returns a class-level recommendation and the evidence supporting its path.
2. Resolve the medication and dose
Reference tables apply allergies, renal function, prior tolerance, and formulation constraints.
3. Run the safety pipeline
Deterministic checks and a separate model review assess the proposed action.
4. Apply the authorization policy
Required clinician approval precedes execution. The system records the decision and schedules follow-up.
Notes: This slide summarizes architecture.md, Sections 3, 4, 13, and 14. The proposed pipeline separates class selection, medication and dose resolution, safety checks, authorization, execution, and follow-up. Staged autonomy is a design assumption, not evidence of clinical validation or prescribing authority.

## Slide 23: 3 Layer Clinical Decision Model
Layer 1 - Traverse Decision Tree
All nodes
resolved?
No
blocked or requires judgment
Yes
some contextual bypasses confidence .70-.95
Yes
all data_lookup confidence > .95
Falls outside tree coverage
Layer 3 - Clinician review
Auto approvable
Safety Pipeline
Layer 2 – RAG Guided
Execute or queue for clinician
Recommendation with citations
Layer 3 - Clinician review
Notes: Decision Trees — designed to handle about 80% of cases. The tree is traversed node by node. If all nodes resolve via data lookup with confidence above 0.95, the recommendation is AUTO_APPROVABLE If some nodes required contextual bypasses and confidence is between 0.70 and 0.95, it goes to CLINICIAN_REVIEW.
A 0.70 confidence means: the tree asked a question (e.g., "Does this patient have heart failure?"), there was no HF diagnosis in the EHR, but the patient is older with risk factors — so we're probably right that the answer is "no," but we're not confident enough to act autonomously on it. Every contextual bypass node in the tree would need its own explicit rule set defining what "high risk" means for that specific question. The criteria for "probably no HF" are different from "probably no renal artery stenosis" or "probably no pheochromocytoma."
Absence of evidence is not evidence of absense

## Slide 24: RAG Uses – patient and clinical
Patient communication
Patient education ("What does Stage 2 hypertension mean?")
Side effect counseling ("I've been having swollen ankles")
Lifestyle coaching ("What dietary changes help?")
Drug explanations ("Why was I started on this drug?")
Decision justification ("Why this drug instead of another?")
Clinical reasoning
Side effect-driven drug changes (e.g. no tree covers "controlled but needs to switch")
Lab-driven dose adjustments ("K+ is 5.1 on ACEi, what to do?")
Comorbidity-specific nuances (diabetes + thiazide metabolic effects)
Notes: Communication uses RAG in every layer — even when the decision tree made the choice, the agent still retrieves guidelines to explain why. Clinical reasoning only happens in Layer 2.

## Slide 25: RAG Constraints
Layer 2 recommendations ALWAYS go to clinician review -- never autonomous
LLM can only cite from uploaded guidelines, not training data
All citations are verified against retrieved chunks before output
Safety layer still runs on Layer 2 recommendations
Audit trail captures exact quotes the AI relied on + retrieval metadata
If guidelines don't address a scenario, AI says "insufficient guidance" (Layer 3)
Notes: These constraints prevent the most dangerous failure mode for a RAG system — hallucinated or unsourced clinical recommendations
All citations are verified against the retrieved chunks before output. If the model claims a guideline says something, the system checks that the retrieved text actually says it.

## Slide 26: Safety Layer – deterministic checks + LLM-as-judge
Dangerous combination (e.g. ACEi + ARB)
Allergy (matches proposed drug and class against allergy list)
Contraindications (e.g. severe asthma for BB)
Lab safety (K, GFR, hCG)
Hypotension and orthostatic risk (recent readings, fall risk)
Side effect history (matches proposed against intolerance list)
Drug interactions (e.g. thiazide + lithium)
Dose ceiling check
Renal dosing adjustment (e.g. if GFR < 30 start ACEi at lowest dose)
LLM-as-judge
  Approve, caution, reject
  Receives patient context, proposed action, decision tree path and/or RAG citations, and results of all 9 preceding safety checks)
  Model from different vendor

## Slide 27
Failure 1: Missed emergency (hypertensive emergency, chest pain)
Defense layer | Mechanism | Catches | Can fail?
Pre-processing layer: Emergency keyword detection | Hard-coded keywords/phrases ("chest pain", "can't breathe", "worst headache", "can't see", etc.) run on every inbound message, ~0ms, no LLM dependency | Direct, unambiguous emergency language | Yes — patient uses non-standard wording ("my chest feels heavy and weird")
Main agent: LLM classification | GPT-4o evaluates messages that don't trigger keywords. Trained to ask targeted follow-ups for ambiguous messages. | Nuanced, indirect, or partial descriptions | Yes — LLM could misclassify or fail to ask the right follow-up
Post-processing layer: Emergency re-scan | Same keyword scan applied to agent's response. If agent's reasoning mentions emergency indicators, catches them even if the agent didn't escalate. | Agent identifies danger in its reasoning but fails to act on it | Yes — only catches keyword matches in the response text
BP reading classification | Deterministic: any reading ≥180/120 → crisis pathway regardless of what the patient says | Numerically dangerous readings even when patient reports "feeling fine" | No — deterministic, cannot fail if reading is recorded
Safety invariant #1 | Emergency keyword scan works even when GPT-4o, Claude, FHIR, and all external services are down | Total system degradation | No — keyword list is in-memory, zero external dependencies
Notes: Residual risk is LOW. The most likely failure scenario — patient uses non-standard phrasing, LLM misclassifies, re-scan doesn't catch it — is mitigated by the keyword list being continuously expanded from real conversations

## Slide 28
BP Above Goal (CONFIRMING_UNCONTROL)
Administer 3-Question Adherence Screener
Check Pharmacy Fill Data
Fills on schedule?
Score?
Combined Assessment
0 (Low Risk)
Missed
Yes
Counsel on Barriers + Proceed
Medium + fills OK
Proceed to Confirm Uncontrolled (out-of-office BP)
Low risk + fills OK
PENDING CLINICIAN
Not improved
THERAPY ADJUSTMENT
Adherence improved but still above goal
AT_GOAL
Reassess
Adherence improved and BP at goal
ADHERENCE INTERVENTION
Identify barriers (2-4 weeks)
8+ (High Risk)
2-7 (Medium)
Any discordance or high risk
Failure 2: Overtreatment (mitigated by adherence gating)
Orthostatic screen (high risk patients)
Interfering substance check (e.g. NSAIDs
Notes: Adherence gating prevents the most common iatrogenic harm: adding drugs to a patient who isn't taking their current ones.

## Slide 29: Data Stores
EHR (FHIR)
Operational
Patient | Condition | MedicationStatement | MedicationDispense | AllergyIntolerance | Observation | Goal | Composition | DocumentReference | Care Plan
Write access: Agent tools (e.g. record_bp_reading), ingestion services (e.g. Surescripts), clinicians
Read access: Orchestrator, Agent (via tools like get_bp_history)
Patient care state | conversation history (e.g. message, tool call, tool result) | decision audit log (e.g. tree traversals) | escalations | follow-up schedules | RAG reasoning logs
Write access: Orchestrator (e.g. state transitions), session summarizer
Read access: Orchestrator, Agent (care thread summaries injected into context)
Vector
Chunked clinical guidelines read by RAG reasoner
AHA 2025
UpToDate
Lookup tables that encode clinical rules
(separates clinical knowledge from code)
Reference Tables
Notes: FHIR resources
**Operational DB** — the system's working memory: patient care state, conversation history with every message and tool call, decision audit logs showing every tree traversal, escalation records, follow-up schedules, and RAG reasoning logs.
**Reference Tables** — 18 lookup tables loaded in-memory at startup. These encode clinical rules: drug classification, dosing, safety thresholds, side effects, single-pill combinations, contraindications, and more. Separating clinical knowledge from code means updating a dosing recommendation doesn't require a code change — you update the table.

## Slide 30: Lookup Table Example
Drug | Class | HTN Start | Titration Steps | Max HTN | Frequency | Tier Map
Lisinopril | ACEi | 10mg | 10 → 20 → 40 | 40mg | Once daily | L=10, M=20, H=40
Enalapril | ACEi | 5mg | 5 → 10 → 20 → 40 | 40mg | Twice daily | L=5, M=10-20, H=40
Losartan | ARB | 50mg | 50 → 100 | 100mg | Once daily | L=50, H=100
Valsartan | ARB | 80mg | 80 → 160 → 320 | 320mg | Once daily | L=80, M=160, H=320
Additional tables:
Drug interactions
Renal dosing adjustments
Disease-specific indications
Single pill combinations
Side effects
BP goal rules
HBPM protocol parameters
Notes: The tier map is critical for the decision trees. When a tree asks "is the patient on a moderate or high dose?", the system looks up the tier map: lisinopril 10mg is low, 20mg is moderate, 40mg is high. This determines whether we uptitrate the current drug or add a new class.
The titration steps encode the exact dose escalation path: lisinopril goes 10 to 20 to 40. The system follows this deterministically — it doesn't ask the LLM what dose comes next.

## Slide 31: Core Data Flows (examples)
Flow 1: Patient submits BP reading
Parse -> validate -> store in FHIR (with position tag if orthostatic) -> classify BP -> assess pulse -> check state machine -> (possibly trigger tree traversal -> safety checks -> execute or queue) -> generate note -> respond to patient
Flow 2: Lab result arrives
Health Gorilla -> normalize to FHIR Observation -> immediate lab safety check against patient's current drugs
  -> CRITICAL: auto-escalate + hold medication + notify clinician + message patient. WARNING: Layer 2 reasoning + queue for clinician.
  -> NORMAL: log, inform patient if follow-up lab.
Pregnancy detection: If lab is HCG AND result is positive/elevated AND patient is on ACEi/ARB → treat as CRITICAL
Flow 3: Side effect report
Patient message -> symptom extraction -> structured side effect lookup (match against current meds) -> RAG counseling narrative -> ask follow-up questions -> if drug change needed: Layer 2 reasoning -> clinician review
Flow 4: Follow-up timer
Scheduler fires daily
  > AWAITING_DRUG_EFFECT + follow-up due -> proactive message
  AT_GOAL + routine check due -> request reading
  LIFESTYLE_ONLY + trial end -> re-evaluate
  Monitoring gaps -> prompt labs
  PENDING_CLINICIAN > 48 hours -> nudge clinician

## Slide 32: Trade-offs
Chose | Over | Because | But
Single agent + policy layers | Multi-agent | Handoff failures are a safety risk | More infrastructure than monolithic single agent, more work to add capabilities
Deterministic trees (80%) | Pure LLM reasoning | Prescribing must be auditable | Overhead of building and maintaining the trees
Cross-provider judge | Same-provider | Model diversity catches correlated failures | Increase in infrastructure, latency
Adherence gating | Escalate immediately | #1 cause of uncontrolled BP is non-adherence | More complicated state machine, slower uptitration
Two-tier emergency | LLM-only | Keywords work when LLM is down | Keyword table to maintain
Graduation path | Start autonomous | Trust built incrementally | More work to assess performance, need to remediate if necessary

## Slide 33: Autonomy is earned (prescribing)
Phase 1
All clinician approval
>250 recs
- 95% approval
- 0 safety rejections
- Judge agreement > 90%
Phase 2
Uptitrate = Autonomous
>500 total
>100 uptitrations
- 95% add drug approval
0 safety rejections
> Judge agreement > 90%
Phase 3
Uptitrate + add = Autonomous

## Slide 34: Autonomy is earned (other)
Record BP reading
Classify BP (deterministic rules)
Lifestyle coaching
Trigger crisis escalation (hard-coded safety layer)
Schedule follow-up (guideline-based intervals)
Order routine monitoring labs (per drug class rules)
Flag monitoring gaps (deterministic)
Patient education (RAG over guidelines)
Notes: Actions where the risk of not acting exceeds the risk of acting are autonomous from the start.
Beyond prescribing, many agent actions are autonomous from Day 1 because they're inherently safe or deterministically controlled:
Recording and classifying BP readings — deterministic rules, no clinical judgment.
Lifestyle coaching — evidence-based guidance, no medication risk.
Triggering crisis escalation — this is a hard-coded safety layer, the faster the better.
Scheduling follow-ups — guideline-based intervals.
Ordering routine monitoring labs — per drug class rules, it's more dangerous to forget the lab than to order it.
Flagging monitoring gaps — deterministic date checking.
Patient education — RAG over guidelines, conversational only, no prescribing implications.

## Slide 35: Final Levels of autonomy
Remove a drug
Down-titrate a drug
Switch drug due to side effect
Resistant HTN management
Crisis management

## Slide 36: Clinician Dashboard
Emergency
Urgent
(critical lab, severe HTN, judge reject)
Same-day
(prescription recs)
Routine
(monitoring gaps, adherence)
Monthly
(patient, performance summaries)
Clinician Queue
Clinician reviews:
Decision tree path
Safety check results
Judge verdict
Patient context
Approve
Execute rec
EHR updated
Patient notified
Follow-up scheduled
Modify
- Clinician adjusts
- delta recorded
Reject
- Log reason
Request info
Agent gathers more data
Item stays in queue
Notes: The goal: a clinician should be able to review and act on a routine prescribing recommendation in under 60 seconds because the system has already done the analysis.

## Slide 37: Follow-up based on care state (sample)
Care state | Follow-up interval | What happens at follow-up | Escalation if missed
AWAITING_DRUG_EFFECT | Monthly (typically 4 weeks) after therapy change | Request BP readings. Ask about side effects. Check if readings are trending toward goal. Per 2025 AHA/ACC Section 5.4 Rec 4: "follow-up at monthly intervals until control is achieved" (COR 1, B-R). | Proactive outreach at due date. If no response within 3 days, flag for care team.
AT_GOAL | 3 months (routine) | Request BP check. Brief symptom screen. Confirm medication adherence. Review any new concerns. | Proactive outreach. If no response, try again in 1 week. After 2 attempts, flag for care team.
LIFESTYLE_ONLY | 3 months initially, extend to 6 months if stable | Request BP check. Review lifestyle progress. Re-evaluate whether medication is needed. | Same as AT_GOAL.
CONFIRMING_UNCONTROL | 4-10 days (HBPM protocol) | Collect ≥12 home readings over ≥3 days (first day discarded). Administer adherence screener. Cross-reference pharmacy fills. Orthostatic screen if high-risk. Day 3 and 7 reminders if insufficient readings. Day 10 timeout → clinician flag + ABPM referral. | Important — uncontrolled BP should not sit unaddressed. Flag for care team after Day 10 timeout.
Notes: The system doesn't let patients fall through the cracks - Each state has a defined escalation if the patient goes silent: proactive outreach, retry, then flag for the care team.

## Slide 38: Lab Monitoring Follow-Up
Two types:
1) Event based gaps (e.g. by medication start, dose increase)
2) Interval-based gaps
Trigger | Labs to order | When | Follow-up
New ACEi/ARB/MRA started or dose increased | K+, Creatinine, eGFR | Baseline (if not recent) + 2-4 weeks post-change (2025 AHA/ACC Section 5.2.8) | Review results when available. Critical value → immediate action. Only a persistent eGFR decline >30% warrants nephrology referral (Section 5.2.9).
New diuretic started or dose increased | K+, Na+, Creatinine | Baseline + 2-4 weeks post-change (2025 AHA/ACC Section 5.2.8) | Same as above. Watch for hypokalemia (thiazide/loop) and hyponatremia (thiazide).
Routine monitoring (ACEi/ARB/diuretic) | K+, Creatinine, eGFR | Every 6 months | Flag as monitoring gap if overdue (Section 14).

## Slide 39: Feedback and Improvement
Recommendation Outcomes
% of patients at goal within 8 weeks of an executed recommendation
% of patients reporting a new side effect within 4 weeks of a therapy change
Clinician approval, modification, and rejection rates
Decision Coverage
% of decisions resolved by decision tree traversal
% of decisions requiring RAG (which nodes are most blocking?) % of decisions escalated to clinician without recommendation
Safety Signals
Rate of side effects / abnormal labs / judge overrides / clinician rejections
Judge Calibration
Agreement matrix vs clinician
RAG Quality
Citation verification pass rate
Zero-citation recommendation rate
Patient Engagement
Outreach messages that resulted in a BP reading within 7 days
Total agent messages THERAPY_ADJUSTMENT to AT_GOAL
Patients Like Me
Once we have sufficient number of patients, build models to predict which patients may do better on particular meds/combos/dosages than others
Notes: Zero-citation recommendation rate catches cases where the LLM made a recommendation without grounding it in guidelines — that should be rare and trending toward zero.
**Patients Like Me** — the long-term vision. Moves beyond guidelines toward personalized treatment selection based on real-world outcomes from similar patients.

## Slide 40
Core Roles
Pre-processing
Patient Message
GPT-4o-mini
Scope Classifier ($0.001/call)
GPT-4o
Conversational Agent ($0.02/call)
Scope Redirect
needs guidelines
tone violation
Post-processing
GPT-4o-mini
Tone Validator ($0.001, –5-10%)
tone violation
response ready
GPT-4o
RAG Reasoner
($0.02/call)
GPT-4o-mini Note Generator
($0.001/call)
after delivery
Claude Sonnet 4.5 LLM-as-Judge ($0.03/call)
prescribing action
Block
APPROVE
CAUTION
Execute
REJECT
Clinician Review
bp_related or ambiguous
off_topic
tone OK
Cost Estimate
Notes: At scale (1,000 patients, ~60% stable, ~30% active, ~10% complex): estimated ~$500/month in LLM costs